## Slide 1: Verification of Cache Coherence Protocols wrt. Trace Filters
Parosh Aziz Abdulla1, Mohamed Faouzi Atig1,
Zeinab Ganjei2, Ahmed Rezine2 and Yunyun Zhu1
1. Uppsala University, Sweden
2. Linköping University, Sweden
FMCAD 2015

## Slide 2: Outline
Transactional memories
Formal model
Small model theorem
  Limit the analysis to a finite number of variables
Verification algorithm for cache coherence
  Backward reachability analysis with monotonic abstraction
Prototype
  Two cache protocols verified

## Slide 3: Transactional Memory

## Slide 4: Transactional Memory (TM)
Init: x = 0
void add() {
atomic {
int t = x;
t = t + 5;
x = t;
}
}
Thread 1
void add() {
atomic {
int t = x;
t = t + 10;
x = t;
}
}
Thread 2
  To simplify concurrent programming
transaction
Notes: Conflict: T1 reading the old value of x and writing x based on the old read value, despite that x has been updated by T2. So T1 cannot commit.
Atomicity: All speculative memory updates of a transaction are either committed or discarded as a unit.
Consistency: The memory operations of a transaction take place in order. Transactions are committed one transaction at a time (in some agreed order).
Isolation: Memory updates are not visible outside of a transaction until the transaction commits data.
Tentative changes

## Slide 5
Thread1
Thread2
commit
commit
abort
Init: x = 0
void add() {
atomic {
int t = x;
t = t + 5;
x = t;
}
}
Thread 1
void add() {
atomic {
int t = x;
t = t + 10;
x = t;
}
}
Thread 2
read x: 0
int t = x;
int t = x
t = t + 5;
x = t;
int t = x;
t = t + 10;
x = t;
t = t + 5
x = t
write x: 5
read x: 0
write x: 10
int t = x
t = t + 10
x = t
Properties of TMs:
  Atomicity
  Isolation
Conflict!
Transactional Memory (TM)
write x: 5
Notes: No animation until the red commit-commit
Two threads writing on the same variable, so one must abort
Atomicity: All speculative memory updates of a transaction are either committed or discarded as a unit.
Consistency: The memory operations of a transaction take place in order. Transactions are committed one transaction at a time (in some agreed order).
Isolation: Memory updates are not visible outside of a transaction until the transaction commits data.
Tentative changes

## Slide 6
Thread1
Thread2
commit
commit
abort
read x: 0
int t = x
t = t + 5
x = t
write x: 5
read x: 0
write x: 10
int t = x
t = t + 10
x = t
Transactional Memory (TM)
write x: 5
  Hardware TM
Init: x = 0
void add() {
atomic {
int t = x;
t = t + 5;
x = t;
}
}
Thread 1
void add() {
atomic {
int t = x;
t = t + 10;
x = t;
}
}
Thread 2
Notes: Hardware transactional memory systems may comprise modifications in processors, cache and bus protocol to support transactions

## Slide 7: Hardware Transactional Memory (HTM)
Conflict manager
  Decide if an instruction
  can be executed
Cache protocol
  Adapted with TM context
Conflict manager
instruction
response
Cache C1
Cache C2
Memory
x
y
z
I
I
I
0
0
0
x
y
z
I
I
I
0
0
0
x
y
z
I
I
I
0
0
0
Thread1
Thread2
commit
commit
abort
int t = x
t = t + 5
x = t
int t = x
t = t + 10
x = t
data
state
line
data
state
line
data
state
line
Notes: Conflict manager: communicates with the program and decides if an instruction can be executed
Cache protocol: after each instruction execution, the state of some cache line is changed according to the transition rules of the protocol

## Slide 8: MESI Protocol
Thread1
write x
Thread2
commit
read x
commit
TMESI Protocol (of FlexTM)
Motivating Example
Conflict manager
instruction
response
x
y
z
I
I
I
0
0
0
x
y
z
I
I
I
0
0
0
x
y
z
I
I
I
0
0
0
TMI
TMI
M
M
M
M
I
M
write x
Thread1
write x
Thread2
commit
write x
commit
Trace not allowed!
abort
Trace allowed
Incoherent states!
Modified
Exclusive
Shared
Invalid
Write within a transaction
Read while another writes within a transaction
Filter
Cache C1
Cache C2
Memory
Commit
Abort
data
state
line
data
state
line
data
state
line
Notes: Mention what a trace is!
Emphasize that the example illustrates the conflict manager is needed
Conflict manager add (filter) in last animation!
Protocol: shows the transitions of the cache line states. Suppose there is only one variable in each cache line here
Tentative write in a transaction -> Tmi state needed -> reflex itomicity
Motivating example: suppose there is no conflict manager -> all the instructions can be executed -> incoherent states reached –> conflict manager needed -> commit in t1 not allowed -> trace allowed
Red (M, M): two threads modifying the same variable at the same time
Conflict manager behaves like a filter

## Slide 9: Goal
Verification of coherence
in presence of filters
Challenges:
  Unbounded number of transactions
  Unbounded number of threads
  Unbounded number of variables
Thread1
write x
Thread2
commit
write x
commit
abort
Conflict manager
instruction
response
Filter
Thread1
.
.
Thread2
.
.
write x
read y
write y
read x
commit
abort
write y
write y
commit
abort
Thread1
.
.
write x
read y
commit
write y
Thread2
.
.
write y
read x
abort
write x
Threadn
.
.
read z
write z
commit
instruction
response
...
write z
...
...
...
...
...
Cache C1
Cache C2
Cache Cn
Memory
Cache C1
Cache C2
Memory
x
y
z
I
I
I
0
0
0
x
y
z
I
I
I
0
0
0
x
y
z
I
I
I
0
0
0
M
I
data
state
line
data
state
line
data
state
line
Cache C1
Cache C2
Memory
x
y
z
I
TMI
I
0
0
0
x
y
z
TMI
I
I
0
0
0
x
y
z
I
I
I
0
0
0
data
state
line
data
state
line
data
state
line
Cache C1
Cache Cn
Memory
x
y
z
I
TMI
I
0
0
0
x
y
z
I
I
TMI
0
0
0
x
y
z
I
I
I
0
0
0
...
data
state
line
data
state
line
data
state
line
Notes: What we verify: all the traces pass the filter do not reach any incoherent state according to the cache protocol

## Slide 10: Contributions

## Slide 11: Contributions
Formal model for protocols with filters
Small model theorem
  Reduces the problem to finite number of variables
Backward reachability analysis
Prototype

## Slide 12: Formal Model

## Slide 13: Formal Model: Cache
Configuration
  Maps each cache line to a state
Transitions:
  Concerns the same cache line of different threads
At least one remote cache line of x is E, TI or I
None remote cache line of x is TMI
All the remote cache lines of x in M transits to S
Cache C1
x
I
TI
y
z
TMI
Cache C2
x
E
I
y
z
I
Cache C3
x
I
I
y
z
I
state
line
state
line
state
line
state
local
remote
remote
I
S
E
I
S
Notes: Mention that transitions are between configurations
Describe the configuration example and avoid defining it
The cache protocol rules consist of the set of the transitions
Horizontal transition: perform the transition on cache c1, which is called the local cache while the other two are called remote caches.
Required: look at the remote cache, if they satisfy the condition; forbidden: no remote cache line is TMI. Then perform the state, and the broadcast should also apply

## Slide 14: Formal Model: Filter
Finite set of forbidden
patterns
write, x, t1
write, x, t2
commit, t1
commit, t2
Forbidden pattern
Filter
Thread1
write x
Thread2
commit
write x
commit
Cache C1
x
I
I
y
z
I
Cache C2
x
I
I
y
z
I
Cache C3
x
I
I
y
z
I
instruction
response
write, x, t1
write, x, t2
read, z, t1
commit, t2
write, y, t2
commit, t2
write, x, t2
write, x, t1
commit, t2
commit, t2
Trace not allowed!
trace
state
line
state
line
state
line
Notes: E.g., a simple trace, that we call a pattern, does not pass the filter. There is a trace in which the pattern exists, so the trace cannot pass the filter either.
A filter does not pass forbidden patterns and the traces in which any forbidden pattern exists

## Slide 15: Small Model Theorem

## Slide 16: Small Model Theorem
Reduces the analysis to a finite number
of variables
Thread1
write x
Thread2
read y
write z
write x
commit
commit
Only x involved
write, x, t1
write, x, t2
commit, t1
commit, t2
Thread1
write x
Thread2
commit
write x
commit
Reaches incoherent state, and passes the filter
Filter
instruction
response
write, x, t1
write, z, t1
write, x, t2
commit, t2
read, y, t2
commit, t1
write, x, t2
write, x, t1
commit, t2
commit, t1
Incorrect
Cache C1
x
I
I
y
z
I
Cache C2
x
I
I
y
z
I
state
line
state
line
E
M
M
M
M
M
Notes: Suppose the filter does not work correctly, there is a trace which reaches incoherent states. We find that only x is involved in the bad states, so we project the trace to x and get a shorter trace with only one variable x. This trace can also pass the filter but reaches the bad state.

## Slide 17: Backward Reachability Analysis

## Slide 18: Well-Structured Transition System
Define a well-quasi-order on configurations
Prove transition relation is monotonic
Provide an algorithm to compute the set of predecessors of an upward closed set
Achievable with techniques
Notes: Pre: compute the set of configurations from which will get the current set of configurations after the transition the is performed

## Slide 19: Well-Structured Transition System
⊑
Conf1
Conf2
Define a well-quasi-order on configurations
Cache C1
x
S
E
z
Cache C2
x
S
I
z
state
line
state
line
Cache C1
x
S
E
y
z
TMI
Cache C2
x
S
I
y
z
I
Cache C3
x
S
I
y
z
I
state
line
state
line
state
line
Notes: Define an ordering -> upward closed sets -> must also be upward closed sets in monotonicity -> ordering not monotonic in our case -> make the set after pre upward closed if it is not, which is called monotonic abstraction
The system is well-structured -> backward reachability can be applied
The algorithm terminates because the order is a well-quasi-order

## Slide 20: Well-Structured Transition System
Due to forbidden sets in transitions
C1
x
I
C2
x
I
C1
x
E
C2
x
I
Prove transition relation is monotonic
C1
x
I
C2
x
I
C3
x
S
⊑
S
Conf1
⊑
Conf3
Conf4
⊑
Conf2
Notes: larger configurations “simulate” smaller configurations
c1 <= c2, and c2->c3, but if there is forbidden{E} in the transition, and c2 contains E, then there is no c4 such that c2->c4 for the same transition

## Slide 21: Well-Structured Transition System
Define a well-quasi-order on configurations
Prove transition relation is monotonic
Monotonic abstraction needed

## Slide 22: Upward Closed Set
Incoherent states representable
by finite caches
With more caches still incoherent
Upward closed sets: symbolic representations
for incoherent states
M
M
M
M
I
M
M
I
I
S
Minimal element
Notes: Set of configurations of incoherent states (bad set): upward closed
Upward-closed sets are preserved in monotonicity

## Slide 23: Backward Reachability Analysis
Start from bad set
Compute the set of predecessors,
and make it upward-closed if needed
Stop if no more new configuration
discovered.
A searching branch closed if
  The minimal element is subsumed
  By an older minimal element
  The trace fails the filter
t1
t2
t2
t3
t1
t3
⊒
Trace (t3, t2) fails the filter
Monotonic abstraction
∩ Init = ∅ ?
Notes: The transitions are different since the sets are different and sometimes only some specific transitions can be performed on the specific set
Compute predecessors (with information of minimal elements)

## Slide 24: Prototype

## Slide 25: Prototype
Extension of Zaama, which implements constrained monotonic abstraction
Applied to
  Two cache protocols
  With six filters
Results obtained a 2.9 Ghz Intel Core i7 with 8GB of RAM

## Slide 26: Experimental Results
UTCP (serial. filter) 70 47 Yes, bad state (M, M) 117.3s
TMESI (serial. filter) 42 38 Yes, bad state (M, M) 35.8s
Cache protocol (filter) #rules #bad states Reachable(Y/N) Execution time

## Slide 27: Conclusion
Formal model for protocols with filters
Small model theorem
  Reduces the problem to finite number of variables
Backward reachability analysis
Prototype

## Slide 28: Thank You