## Slide 1: Universal Boolean Functional Vectors
Jesse Bingham
FMCAD 2015
Austin, Texas, USA

## Slide 2
?
  “… I see the theoretical contribution in this paper as a very personal view of something very intuitive (and standard)” -Anonymous Reviewer, 2015
  “Somebody needs to be killed for the title of your paper.” -Non-anonymous Colleague, 2015
  “… this difficulty also arises in circuits containing shifters where the shift amount depends on the data, such as in a floating point alignment unit. Multiplication is a particularly difficult function, ...” -Randy Bryant, 1998

## Slide 3: This Talk Has Three Parts
Summary of Approach – meant to be accessible by all
Case Study: Floating Point Addition
Main Theoretical Result
Please see paper for related work, mathematical rigor, further experiments, and whatever else is in there
Assumption: you have some clue what a BDD is.

## Slide 4: Summary of Approach

## Slide 5: In a Nutshell…
Might be
exponentially big
All of tractable size
secondary
variables
primary
variables

## Slide 6: What about Soundness?
=?
=?
Clearly,
But we only have
when is universal

## Slide 7: Universality
Said another way: universality means that, when viewed as
a function from -assignments to -assignments, is surjective
0
1
0
…
For all
output patterns
1
1
0
…
There exists an
input pattern
such that
If is universal, we call it a UBFV, and we
call a UBFV representation of

## Slide 8: Results
Theory
  Any function that can be tractably represented using a partitioned BDD has a tractable UBFV representation
    Corollary: represent the hidden-weighted bit function tractably
  Cute: any (non-constant) single-output function has a UBFV representation that is just a variable
    Might involve exponentially large UBFV BDDs
Practice
  Huge impact on proofs of Floating-Point Addition Hardware
    E.g. double precision: reduced proof run-time from 50 hours to ½ hour
    Allows for packed FADD operations to be verified end-to-end
  Ditto for Fused-Multiply Add (FMA) designs
  Also: normalizing floating point hardware, string instructions
  Several approaches to verifying universality

## Slide 9: Case Study: Floating Point Addition

## Slide 10: Floating Point Addition (FADD)
sign
exponent
mantissa
Value represented is

## Slide 11: FADD with BDDs
Integer addition: if variable order interleaves the bits from both inputs, you get linear sized BDDs
FADD: because of the data-dependent (ediff) alignment, there is no good variable order
  BDDs for FADD are exponential for any order
Standard solution: case split based on ediff
28 cases

## Slide 12: A UBFV for FADD
variables
Extract middle
bits from shifter
BDDs over the variables
Shift right by ediff
(negative
ediff shifts left)
A
Importantly,
this is
universal

## Slide 13
Moderate BDDs
FADD
circuit
Normalizer & Rounder
Trivial BDDs
Moderate BDDs
bit only depends on
and variables

## Slide 14: In Summary
The FADD UBFV just presented involves variables
Intuition: is the bit of the second input’s mantissa that aligns with bit of the first after alignment
The variable order that interleaves the variables with the variables results with BDDs behavior similar to integer addition
Normalization and Rounding do not introduce significant additional complexity
Hence we can verify FADD instructions without case splitting, by symbolically simulating with this UBFV

## Slide 15: Results
Comparison of UBFV-approach vs classical case-splitting approach, for SSE Scalar FADD instructions (recent Intel design)
For single instruction multiple-data (SIMD) instructions it is also effective
  Allows for elimination of decomposition cut-point
See paper for results on other instructions, such as Fused-Multiply Add

## Slide 16: Theory: Partitioned BDDs and UBFV Representations

## Slide 17: Summary of Theorem
Partitioned BDDs represent a function by a set of BDDs, each can employ a different variable order
  Basically a formalization of BDD case-splitting
There exist functions that have tractable partitioned BDDs that don’t have tractable BDDs
  Floating point addition, hidden weighted bit, etc
Theorem: any partitioned BDD has a UBFV representation (a single BDD) with at most a polynomial increase in size
  Furthermore, the UBFV only has logarithmically more secondary variables
  Promotes BDD node “sharing” across partitions

## Slide 18: Partitioned BDDs




BDDs over n variables
…
different
variable
orders
: ith case split
: represents f within wi

## Slide 19: UBFV Representation Construction
0
1
Three-fold Trickery:
log2(k) secondary variables select one of the k partitions
Secondary variables y1,…,yn are such that in each partition, yi corresponds to the ith primary variable in the partition’s order
jth partition becomes BDD for generalized co-factor of fj with respect to wj, which has size at most |fj||wj|.

## Slide 20: So… If you are doing case-splitting/partitioning on BDDs, you should chuck that out and use a UBFV instead.

## Slide 21: Thank you