## Slide 1
Template-based Synthesis of Instruction-Level Abstractions for SoC Verification
Pramod Subramanyan, Yakir Vizel, Sayak Ray and Sharad Malik
FMCAD 2015
On-chip Interconnect
CPU
GPU
Camera
Touch
Flash
DMA
WiFi/3G
GPS
…
MMU+
DRAM
ISA
ILA
ILA
ILA
ILA
ILA
ILA
ILA
ILA
ILA
ILA
This work was supported in part by CFAR, one of the six SRC STARTnet centers, sponsored by MARCO and DARPA

## Slide 2: Why an ILA?
On-chip Interconnect
CPU
GPU
Camera
Touch
Flash
DMA
WiFi/3G
SCIP
…
MMU+
DRAM
Firmware running on the microcontroller orchestrates the operation of each unit
Microcontroller
Memory
HW accelerators
…
NoC interface

## Slide 3: Why an ILA?
μC registers
ALU
Inst Seq.
AES mem range
RSA mem range
SHA mem range
…
Interconnect
Private Memory
Memory
Microcontroller
Memory
HW accelerators
…
NoC interface
FW uses memory-mapped I/O to monitor/control HW
Insight: Treat MMIO reads/writes as part of an extended ISA aka ILA

## Slide 4: Why an ILA?
; start AES state machine
MOV ACC, #01
MOV DPTR, #0xFF00
MOVX @DPTR, ACC
; poll for completion
wait_finish:
MOV DPTR, #0xFF01
MOVX ACC, @DPTR
CMPI ACC, #00
JNZ wait_finish
IDLE
READ
ENC
WRITE
Instruction-Level Model of µc ISA
Instruction-Level Model of HW accelerators
Instruction-Level Abstraction (ILA) of SoC
“Instruction” is now any firmware-visible state update triggered by some event

## Slide 5: What does the ILA look like?
For a microcontroller
REGS
ROM
PC
Input State
Output State
REGS
PC
RAM
RAM
Transition Relation
opcode = ROM[PC];
switch (opcode)
{
case 00:
REGS[ACC] = ...;
REGS[R0] = ...;
REGS[FLAGS] = ...;
case 01:
REGS[ACC] = ...;
REGS[R0] = ...;
REGS[FLAGS] = ...;
...
}

## Slide 6: What does the ILA look like?
For a hardware accelerator
curstate
rdcnt
rdptr
Input State
Output State
wrptr
Transition Relation
switch (curstate)
{
case IDLE:
if (rdaddr == RDPTR_ADR)
rdptr = datain;
...
case READ:
...
case AES1:
...
case AES2:
...
case WRITE:
...
}
wrlen
rdbuf
wrbuf
...
curstate
rdcnt
rdptr
wrptr
wrlen
rdbuf
wrbuf
...

## Slide 7: Our Contributions
Template abstraction
Synthesis Algorithm
Instruction-Level Abstraction
Simulator
Golden Model
RTL
Model Checker
Refinement Relations
Bugs/counter examples
FW verification
Challenges in constructing the ILA
ILA must completely define HW behavior
Manual construction is tedious and error-prone
(2) Template language and Synthesis algorithm
(3) Verifying ILA correctness
(1) Concept of the ILA
New components
Existing components
Automatically generated
Existing tools

## Slide 8: ILA Synthesis using Program Synthesis
Build on recent progress in the area of program synthesis [ASPLOS’06, ICSE’10, FMCAD’13, …]
loop (??) {
x = ( x & ??) + ((x >> ??) & ??);
}
return x;
x = (x & 0x5555) + ((x >> 1) & 0x5555);
x = (x & 0x3333) + ((x >> 1) & 0x3333);
x = (x & 0x0077) + ((x >> 1) & 0x0077);
x = (x & 0x000F) + ((x >> 1) & 0x000F);
return x;
Transform a template-program with “holes” into a complete program using an I/O oracle

## Slide 9: Synthesizing the ILA
Template abstraction
Synthesis Algorithm
Instruction-Level Abstraction
Simulator
Main idea: synthesize the ILA from a template!
Simulator is the I/O oracle
Equivalent of the program with “holes”
How do we scalably synthesize ILAs?
Template language and synthesis formulation have to be designed carefully.

## Slide 10: Template Language
Input State
Output State
Template ILA partially defines the transition relation between input and output states
Defined by the verification engineer
Synthesis parameter: curstate Enables modular synthesis of transition relation
curstate
rdcnt
rdptr
wrptr
wrlen
rdbuf
wrbuf
...
curstate
rdcnt
rdptr
wrptr
wrlen
rdbuf
wrbuf
...

## Slide 11: Template Language: Choice Primitive
R0-R7
ALU
opcode
op
imm
An Example Template
SRC1 = choice src1 [R0 … R7, IMM]
SRC2 = choice src2 [R0 … R7, IMM]
ADD_RES = SRC1 + SRC2
SUB_RES = SRC1 – SRC2
INC_RES = SRC1 + 1
…
ALU_RES = choice alu_result [ADD_RES, SUB_RES, INC_RES, … ]
What is missing?
No mapping of opcodes to operations
No mapping of opcode bits to register values, immediates, etc.
Synthesis algorithm can infer these details using simulation results!

## Slide 12: Template Language: Choice Primitive
R0-R7
ALU
opcode
op
imm
An Example Template
switch (opcode)
case 00: ALU_RES = R0 + IMM;
case 01: ALU_RES = R1 + IMM;
…
case FF: ALU_RES = R7 – R0
}
Synthesis algorithm
SRC1 = choice src1 [R0 … R7, IMM]
SRC2 = choice src2 [R0 … R7, IMM]
ADD_RES = SRC1 + SRC2
SUB_RES = SRC1 – SRC2
INC_RES = SRC1 + 1
…
ALU_RES = choice alu_result [ADD_RES, SUB_RES, INC_RES, … ]

## Slide 13: Summarizing the Template Language
Expressions with bitvector and array datatypes (QF_ABV)
Plus 3 synthesis primitives
choice id [c1, c2, … , ck]
Replace this expression with one of c1 … ck
bv-in-range START END
Replace with a bitvector bv s.t. START <= bv <= END
read-slice-choice id bv-exp size
Replace with a subvector of bv-exp of width size

## Slide 14: Synthesis Algorithm: CEGIS
Family of relations defined by template
Counter-example Guided Inductive Synthesis (CEGIS)
Find distinguishing input: results in different outputs for some two relations
Evaluate simulator output for the distinguishing input
Eliminate functions from family which are inconsistent with simulator output
Repeat until distinguishing inputs cannot be refined any more

## Slide 15: Synthesis Algorithm on Toy Example
R0
ALU
opcode
R1
mux
R0
SRC2 = choice src2 [R0, R1]
ADD_RES = R0 + SRC2
SUB_RES = R0 – SRC2
R0_NEXT = choice alu_result [ADD_RES, SUB_RES]
8
8
2
Iteration | Opcode | R0_in | R1_in | R1_out
#1 | 0 | 0 | 0xE8 | 0
#2 | 0 | 0x68 | 0 | 0xD0
switch (opcode) {
case 0: R0 = R0+R0;
case 1: R0 = R0-R0;
case 2: R0 = R0+R1;
case 3: R0 = R0-R1;
}
Synthesized ILA
R0=R0+R0
R0=R0-R0
R0=R0+R1
R0=R0-R1
After iteration #1
After iteration #2

## Slide 16: Correctness of the ILA
Template abstraction
Synthesis Algorithm
Instruction-Level Abstraction
Simulator
RTL
Defines a family of ILAs
Potential Problems:
Simulator behavior may not lie within the family defined by the template
Simulator/RTL mismatch
ILA/RTL mismatch

## Slide 17: Synthesis Correctness
Template abstraction
Synthesis Algorithm
Instruction-Level Abstraction
Simulator
If simulator behavior falls within the family functions defined by the template, then the synthesized ILA is equivalent to the simulator.
Defines a family of ILAs

## Slide 18: Verifying the ILA
Template abstraction
Synthesis Algorithm
Instruction-Level Abstraction
Simulator
Golden Model
RTL
Model Checker
Refinement Relations
“Golden model” is automatically generated from the ILA
Refinement relations are written by the verification engineer and specify that ILA and golden model have equivalent I/O behavior

## Slide 19: Refinement Relations for ILA Verification
From [McMillan, 1999]
Golden model only “executes” when inst_finished=1
if (inst_finished) {
ACC = …
PC = …
R0 = …
} else {
// do nothing
}
Relations are in the following form:
G (inst_finished => (gm.ACC == oc8051.ACC) )
G (inst_finished => (gm.R0 == oc8051.R1) )
...
8051 Verilog Golden Model
oc8051 RTL
ROM
inst_finished
=
Model Checker
Compositional refinement relations enable scalable verification

## Slide 20: Test Case: Example SoC
8051 ILA
AES+SHA+XRAM ILA
Consists of components from OpenCores.org and OpenCrypto project
Created two ILAs: 8051 core and AES+SHA+XRAM

## Slide 21: Implementing the Framework
Template abstraction
Synthesis Algorithm
Instruction-Level Abstraction
Simulator
Golden Model
RTL
Model Checker
Refinement Relations
FW verification
Python library using Z3
ABC
Yosys
Python library
Yosys
i8051sim
[UC Riverside]
Python simulator for AES+SHA+XRAM
OpenCores.org OpenCrypto
Tools/components developed by us
Existing* tools and components

## Slide 22: Summarizing Synthesis Results
Templates are fairly easy to write: several hundred LoC
Synthesis usually done in tens of seconds; worst case is a few hours
Helps validate simulator: 6 bugs were found

## Slide 23: Summarizing Verification Results
Initial Model
BMC up to 17 cycles (5-6 insts) in 5 hours
Compositional Model
BMC up to depth of 35 cycles in 2000s
Found six RTL bugs
Proved (PDR) 56-238 instructions correct

## Slide 24: In Conclusion
Template abstraction
Synthesis Algorithm
Instruction-Level Abstraction
Simulator
Golden Model
RTL
Model Checker
Refinement Relations
FW verification
Found many non-trivial bugs
Can build complete ILA with manageable effort
Can be proven correct
  https://bitbucket.org/spramod/fmcad-15-soc-ila
Applied on commercial SoCs with promising results

## Slide 25
Backup Slides

## Slide 26: Conclusion
Methodology for Synthesizing Instruction-Level Abstractions for SoC verification
What we have shown:
  Methodology can find real bugs
  Helps define precise and complete semantics for HW behavior
  Prove that the ILA matches the HW behavior
  All with a manageable amount of effort
Has been applied on commercial designs
  Found bugs there too!
Lots more details in the paper!
  https://bitbucket.org/spramod/fmcad-15-soc-ila

## Slide 27: 8051 ILA: Synthesis Results (1/3)
Synthesis parameter is the opcode (# of opcodes = 256)
Model | LoC | Size (kB)
Template ILA | ~650 | 30 kB
C++ simulator | ~3000 | 106 kB
Behavioral Verilog | ~9600 | 360 kB
Size of the Template ILA

## Slide 28: 8051 ILA: Synthesis Results (2/3)
State | Avg Time (s) | Max Time (s)
ACC | 4.3 | 8.5
B | 3.6 | 5.1
DPH | 2.7 | 5.0
DPL | 2.6 | 4.4
IRAM | 1245.7 | 14043
P0 | 1.8 | 2.7
P1 | 2.4 | 3.8
P2 | 2.2 | 3.5
P3 | 2.7 | 4.6
PC | 6.3 | 141.2
PSW | 7.3 | 15.9
SP | 2.8 | 5.0
XRAM/addr | 0.4 | 0.4
XRAM/dataout | 0.3 | 0.4
Synthesis times for each opcode

## Slide 29: 8051 ILA: Synthesis Results (3/3)
Synthesis detects bugs if simulations results inconsistent with the family of functions defined by template ILA
Found 5 bugs in the simulator
Signed/unsigned confusion in C++ [CJNE, DIV, DA]
  RAM[RAM[i]]: RAM is a signed char array
  tempAdd = RAM[ACC] + 0x60: tempAdd is short int
Typo in AJMP
DIV/0 definition was incorrect
Methodology forces us to precisely define the semantics for each instruction

## Slide 30: 8051 ILA: Initial Verification Setup
Golden model only “executes” when inst_finished=1
if (inst_finished) {
ACC = …
PC = …
R0 = …
} else {
// do nothing
}
Properties in the following form:
G (inst_finished => (gm.ACC == oc8051.ACC) )
G (inst_finished => (gm.R0 == oc8051.R1) )
...
8051 Verilog Golden Model
oc8051 RTL
ROM
inst_finished
=
Model Checker
Automatically generated Verilog golden model from ILA
ROM is non-deterministically initialized
RAM size was reduced from 256b to 16b

## Slide 31: 8051 ILA: Initial Verification Results
6 RTL bugs were found
  AJMP: PC used in target addr calc was a few bytes ahead
  Decoding bugs in JB/JBC/JNB
  Undefined SFR addresses return last read value
  Back-to-back reads of same SFR addressed in different ways
SETB 0xD7
CPL C
ADDC A, B
Set carry flag
Complement carry flag
Read carry flag
Reached BMC bound of 17 cycles in 5 hours
17 cycles is about 5-6 instructions

## Slide 32: 8051 ILA: More Scalable Verification
Using compositional reasoning [McMillan 2001]
Generate a golden model for each opcode (256 models)
Implementation of other opcodes is abstracted away
clk
acc
ram
P0
opcode=05
State Must Match Again
Pick a certain point in time
Suppose all instructions have been executed correctly until this point
And now we receive opcode = 05
Will this opcode be executed correctly?
We make this argument for every opcode and every state element

## Slide 33: 8051 ILA: More Scalable Verification
Using compositional reasoning [McMillan 2001]
Generate a golden model for each opcode (256 models)
Implementation of other opcodes is abstracted away
clk
acc
ram
P0
opcode=05
State Must Match Again
LTL formula:
is a formula which says that all state until now matches
Sg is the value of the state element in the golden model
Sr is its corresponding value in the RTL

## Slide 34: 8051 ILA: Final Verification Results
Property | BMC Bounds |  |  |  |  | Proofs
 | CEX | ≤ 20 | ≤ 25 | ≤ 30 | ≤ 35 | 
PC | 0 | 0 | 25 | 10 | 204 | 96
ACC | 1 | 0 | 8 | 39 | 191 | 56
IRAM | 0 | 0 | 10 | 36 | 193 | 1
XRAM/data | 0 | 0 | 0 | 0 | 239 | 238
XRAM/addr | 0 | 0 | 0 | 0 | 239 | 238
Much higher BMC bounds and quite a lot of instructions proven correct!

## Slide 35: What does an SoC consist of?
On-chip Interconnect
CPU
GPU
Camera
Touch
Flash
Many units interacting with each other through an on-chip interconnect
DMA
WiFi/3G
SCIP
…
MMU+
DRAM

## Slide 36: Example SoC “Flow”
CPU
GPU
Camera
Touch
Flash
DMA
WiFi/3G
SCIP
…
MMU+
DRAM
SCIP programs DMA to read from flash
DMA writes command to flash
Flash returns data to memory
SCIP locks memory region
SCIP fetches data and checks signature
…

## Slide 37: Verifying System-Level Properties
CPU
GPU
Camera
Touch
Flash
DMA
WiFi/3G
SCIP
…
MMU+
DRAM
SCIP programs DMA to read from flash
DMA writes command to flash
Flash returns data to memory
SCIP locks memory region
SCIP fetches data and checks signature
…
Verification Requires
Model of the μc ISA
Model of DMA controller
Model of the flash device
Model of the MMU
Model of SCIP crypto HW
…
Different from software verification because we need to model all the hardware state machines and “special” reads and writes to memory-mapped I/O locations

## Slide 38: Challenges in Constructing an ILA
Must be precisely-defined and complete
  Security bugs lurk in corner cases, undefined behavior, illegal ops
Must match hardware behavior
  ILA must be verifiable
  If hardware doesn’t match ILA, proofs made with it are invalid!
Past work suggests manual construction which is
  Error-prone
  Cannot be verified to be correct
  Extremely tedious to construct

## Slide 39: Complexity in the Combinatorial Explosion
Individual expressions are mostly straightforward
REGS
ROM
PC
Input State
Output State
REGS
PC
RAM
RAM
Transition Relation
opcode = ROM[PC];
switch (opcode)
{
case 00:
REGS[ACC] = ...;
REGS[R0] = ...;
REGS[FLAGS] = ...;
case 01:
REGS[ACC] = ...;
REGS[R0] = ...;
REGS[FLAGS] = ...;
...
}
Combinatorial explosion that occurs – as we have to define everything for every opcode – makes the ILA hard to construct manually
opcode = ROM[PC];
switch (opcode)
{
case 00:
REGS[ACC] = ...;
REGS[R0] = ...;
REGS[FLAGS] = ...;
case 01:
REGS[ACC] = ...;
REGS[R0] = ...;
REGS[FLAGS] = ...;
...
}

## Slide 40: Generate ILA automatically?
Simulator
HW (RTL) Implementation
Static Analysis
Synthesized ILA
Unfortunately this is not practical for realistic designs

## Slide 41: Why Is Verification Required?
“Ideal” ILA
ILA defined by simulator
HW (RTL) Implementation
Template ILA Family
In an ideal world, all of these are the same and no verification is needed!
But back in the real world, none of these are probably equal to any of the others! And so we do need verification.

## Slide 42: Synthesis Algorithm Correctness
ILA defined by simulator
Template ILA Family
If
Then
Synthesized ILA
ILA defined by simulator
But note, we still don’t know if
HW (RTL) Implementation
Synthesized ILA

## Slide 43: Verification Ensures That
HW (RTL) Implementation
Synthesized ILA
This ensures that any firmware properties verified using the ILA are valid

## Slide 44: But What If
HW (RTL) Implementation
Synthesized ILA
“Ideal” ILA
As long as we can prove that our system-level properties hold, it doesn’t matter!

## Slide 45: How is Verification Done?
Write Refinement Relations to prove that the ILA and HW implementation have identical input/output behavior
Refinement relations can be scalably model checked using compositional reasoning [McMillian, 2000]
Details in the paper