## Slide 1: Compositional Reasoning Gotchas in Practice
CHIRAG AGGARWAL, OSKI TECHNOLOGY
PAUL HYLANDER, IKANOS
YOGESH MAHAJAN, NVIDIA
JON MICHELSON, NVIDIA
VIGYAN SINGHAL, OSKI TECHNOLOGY

## Slide 2: Formal Property Verification on Large Designs
Large designs; typically involving the work of multiple designers
Large number of properties to be checked
Compositional assume-guarantee reasoning fits naturally
Divide-and-conquer addresses some tool capacity concerns
M1
M2
S
Environment
Constraints
Properties to check on S
+
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 3: Compositional Reasoning
M1
M1 Unit level
constraints
Properties to check on M1
+
{
}
,
M2
M2 Unit level
constraints
Properties to check on M2
+
M1
M2
S
Environment
Constraints
Properties to check on S
+
decomposition
{
}
inference rule
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 4: ARM® AMBA® AXI4 WSTRB Interface
AR (Read Address)
AW (Write Address)
AXI4 Slave
R (Read Data)
B (Write Response)
W (Write Data)
AXI4 Master
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 5: R and B Channels
R Channel (Read Response)
  Supports reads of multiple beats (cycles)
  RVALID asserted on every cycle of data
  RLAST indicates last beat
  RREADY acknowledges receipt
RVALID
RDATA
RLAST
64
RREADY
M
S
BVALID
BRESP
2
BREADY
M
S
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.
B Channel (Write Response)
  Always 1 beat
  BVALID asserted with BRESP
  BREADY acknowledges receipt

## Slide 6: R and B Channels
RVALID
RDATA
RLAST
64
RREADY
M
S
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 7: Simplified Version of a Real Master-Slave Design
Master RTL
  Single FIFO to store R and B Responses
  FIFO sized to twice the length of longest R burst length
  R beats not dequeued until after RLAST arrive
  Once RLAST arrives, all R beats and B responses dequeued
  When the FIFO is full, RTL back-pressures BVALID
Slave RTL
  Single FIFO to store R and B Responses
  FIFO is 2-deep
  R beats or B responses dequeued as Master receives previous transactions
R1.1
R1.1
R1.1
R1.1
R1.1
R1.1
B1
B2
R1.L
R1.1
R1.1
R1.1
R1.1
B3
M
S
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 8: Deadlock in a Real System
Master RTL
  Single FIFO to store R and B Responses
  FIFO sized to twice the length of longest R burst length
  R beats not dequeued until after RLAST arrive
  Once RLAST arrives, all R beats and B responses dequeued
  When the FIFO is full, RTL back-pressures BVALID
Slave RTL
  Single FIFO to store R and B Responses
  FIFO is 2-deep
  R beats or B responses dequeued as Master receives previous transactions
R1.1
R1.1
R1.1
R1.1
R1.1
R1.1
B1
B2
B3
B4
R1.2
S
M
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 9: Deadlock in a Real System
R1.1
R1.1
R1.1
R1.1
B1
B2
R1.2
S
M
If either M or S is “fixed”, system M ⊗ S will work!
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 10: But Will We Catch It with Formal Verification?
Master Property m1:
  Once the master receives BVALID, eventually it must assert BREADY
Slave property s1:
  Once the slave sends an accepted RVALID with no RLAST, eventually the slave must send RVALID with RLAST asserted
property master_liveness_bready;
@(posedge aclk) disable iff (!aresetn)
(bvalid && !bready) |->
s_eventually bready;
endproperty
property slave_liveness_rlast;
@(posedge aclk) disable iff (!aresetn)
(rvalid && !rlast && rready) |->
s_eventually (rvalid && rlast);
endproperty
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 11: But Will We Catch It with Formal Verification?
Master Property m1: Once the master receives BVALID, eventually it must assert BREADY
Slave property s1: Once the slave sends an accepted RVALID with no RLAST, eventually the slave must send RVALID with RLAST
M
% assume s1
% prove m1
% assume m1
% prove s1
S
Both pass!!!
User concludes m1 and s1 are each true on the system M ⊗ S!
DUT
DUT
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 12: Compositional Reasoning
M1
M1 Unit level
constraints
Properties to check on M1
+
{
}
,
M2
M2 Unit level
constraints
Properties to check on M2
+
M1
M2
S
Environment
Constraints
Properties to check on S
+
decomposition
{
}
inference rule
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 13: Compositional Reasoning Concerns
Soundness is a major concern!
  Nobody wants to use an unsound approach …
  Do not want to burden end-users with potential soundness issues
Cost of deployment is a concern
  Methodology impact
  Property decomposition effort
  Capturing Interface Properties and Invariants
Completeness is a lesser concern
  So long as it is cheap to detect these cases, a determined user can figure out some other approach
Should be tool-agnostic
  No quirky tool-specific semantics that make it hard to reason about compositional proofs
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.
Notes: Soundness : will we make incorrect claims about S based on results seen on M1 and M2?
Completeness: can every property of interest on S be proven using reasoning which fits the schema of the rule?

## Slide 14: Simplified McMillan’s Compositional Reasoning Rule
To check whether properties hold on S, suffices to
Set up new target properties consistent with some partial order on
  Note that and
For each , use a suitable abstraction of S to prove that must be true at whenever H is true at all
0
1
2
n
n+1
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 15: McMillan’s Rule: It is Sound and It Works!
This is a sound rule!
Can be used with both liveness and safety properties
For the AXI example, we have
  2 properties: the master property and slave property
  2 possible orderings of {,} to consider
  2 abstractions to consider : either AXI master or AXI slave is blackboxed
For each possible application of McMillan’s rule, at least one of the checks fails for the AXI example
fails with slave blackboxed, proven with master blackboxed
fails with either master or slave blackboxed
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.
Notes: Mention which property does not hold for the AXI system

## Slide 16: McMillan’s Rule: Some Concerns
Takes effort to explicitly order the properties
  for a large number of properties
  maintaining that order throughout RTL development
… and to detect/handle cases for which no ordering works
  The rule is incomplete with liveness properties [see Trefler2000 for an example]
It’s a complicated rule – how can the end-user confirm that the rule has been applied soundly?
  User might not be intimately familiar with the language semantics (e.g. SVA)
  Tools must obey the semantics of the language
  User might not be aware of all the assumptions under which the rule is valid
    e.g. Does the rule apply when reasoning about finite traces? Under what semantics?
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.
Notes: There are cheaper alternative rules that can be used profitably ...

## Slide 17: An “Unsound” Approach (a Common Practice)
A_foo: assume p1;
B_foo: assert p2;
A_foo: assert p1;
B_foo: assume p2;
A
B
A_foo: assert p1;
B_foo: assert p2;
A
B
{
}
{
}
,
infer proof results for asserts after
factoring in bounded proof depths
Naming convention to manage assumes/asserts
Unsound for liveness
Unsound for safety in some cases
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 18: An “Unsound” Approach: It Works!
No need to explicitly order the properties
Minimal methodology impact with use of naming convention
Focus on safety properties
Users need to watch out for the pitfalls (!)
Circularity is at its heart
  Combinational loop in A1 and B1 is reported by most tools
  p1 gets proven on A2 after assuming p2 and p3 (with suitable reset state)
  p2 and p3 get proven on B2 after assuming p1
  Most tools do not complain about this latter case
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 19: Who Will Check for Soundness?
I prowl in the dark and make no sound!
"But let me ask one question: Who will bell the Cat?"
http://www.gutenberg.org/files/19994/19994-h/19994-h.htm#Page_15
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.
Notes: Just something funny … this is the last talk of the session, after all.

## Slide 20: Dead-ends: Infinite Traces in a DUT
R
R
1
1
1
1
∞
∞
∞
. . .
. . .
∞
. . .
∞
. . .
∞
. . .
∞
. . .
∞
. . .
. . .
∞
∞
. . .
. . .
. . .
∞
. . .
∞
R
1
1
1
1
2
2
2
2
2
2
2
2
2
2
2
2
Every trace
is infinite!
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.
Notes: [[Measuring coverage in formal: Checkers, Constraints, Complexity and Abstractions ]]

## Slide 21: Dead-ends: Constraints Eliminate Partial Traces
R
R
1
1
1
1
∞
∞
∞
. . .
. . .
∞
. . .
∞
. . .
∞
. . .
∞
. . .
∞
. . .
. . .
∞
∞
. . .
. . .
. . .
∞
. . .
∞
R
1
1
1
1
2
2
2
2
2
2
2
2
2
2
2
2
Traces dropped
Traces dropped
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.
Notes: [[Measuring coverage in formal: Checkers, Constraints, Complexity and Abstractions ]]

## Slide 22: … Sometimes Causing Dead-Ends
R
R
1
1
1
1
∞
∞
∞
. . .
. . .
∞
. . .
∞
. . .
∞
. . .
∞
. . .
∞
. . .
. . .
∞
∞
. . .
. . .
. . .
∞
. . .
∞
R
1
1
1
1
2
2
2
2
2
2
2
2
2
2
2
2
Level 1 dead-end
Level 2 dead-end
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.
Notes: [[Measuring coverage in formal: Checkers, Constraints, Complexity and Abstractions ]]

## Slide 23: Dead-end in a Sequence Detector
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  | 
b
cycle
C1
C3
For satisfying C1, b should be 0
For satisfying C3, b should be 1
Conflicting constraints cause dead-end!
Constraints
C1: b should not be high in back to back cycles
C2: b should be high at most 2 times in a window of 6 cycles
C3: b should be high at least 3 times in a window of 12 cycles
Dead-end starts from here
Can be avoided with constraint:
C4: b should be high at least once in a window of 6 cycles
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 24: Intentional Dead-ends
Constraint: never assert or de-assert a for 3 consecutive cycles
B
D
C
E
A
ERR
a
a
a
a
a
!a
!a
!a
!a
!a
no_ERR_c: assume property (
@(posedge clk) disable iff (!rstn)
(sm != ERR)
);
no_D_c: assume property (
@(posedge aclk) disable iff (!aresetn)
(sm == D) |-> (!a)
);
no_E_c: assume property (
@(posedge aclk) disable iff (!aresetn)
(sm == E) |-> a
);
We prefer constraints that avoid dead-ends, e.g.:
Some tools trim dead-ends, others do not!
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 25: Dead-end Trimming Results in a Missed Bug
Bug: B sends pop when ctr is 0, but this bug occurs only when push is 0
For the failing scenarios of B_no_undeflow:
  ctr wraps around to 15 and will cause violation of assumption A_no_overflow
If formal tool trims this dead-end, bug escapes!
  Compositional semantics with dead-end trimming are suspect!
Caught if constraints written to avoid dead-ends:
logic [3:0] ctr;
always @(posedge clk or negedge rstn) begin
if (!rstn) ctr <= 0;
else ctr <= ctr + push - pop;
end
A_no_overflow: assert property(
@(posedge clk) disable iff(!rstn)
ctr <= 4’h8
);
B_no_underflow: assert property(
@(posedge clk) disable iff(!rstn)
pop <= ctr
);
A
B
0
1
2
3
4
5
6
7
push
data
pop
ctr
TB
A_no_overflow: assert property(
@(posedge clk) disable iff(!rstn)
(ctr == 8) |-> !push
);
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 26: Verifying our AXI System with Safety Properties
Master Property m1s:
  Once the master receives BVALID, eventually it must assert BREADY (within B_TIMEOUT cycles)
Slave property s1s:
  Once the slave sends an accepted RVALID with no RLAST, eventually the slave must send RVALID with RLAST asserted (within R_TIMEOUT cycles)
property master_safety_bready;
@(posedge aclk) disable iff (!aresetn)
(bvalid && (!bready)) |->
##[1:‘B_TIMEOUT] bready;
endproperty
property slave_safety_rlast;
@(posedge aclk) disable iff (!aresetn)
(rvalid && (!rlast) && rready) |->
##[1:‘R_TIMEOUT] (rvalid && rlast);
endproperty
RVALID
RLAST
RREADY
BVALID
BREADY
M
S
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 27: But Will We Catch It with Formal Verification?
Master Property m1s: Once the master receives BVALID, eventually it must assert BREADY
Slave property s1: Once the slave sends an accepted RVALID with no RLAST, eventually the slave must send RVALID with RLAST
M
% assume s1s
% prove m1s
% assume m1
% prove s1
S
Both pass!!!
User concludes m1 and s1 are each true on the system M ⊗ S!
DUT
DUT
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 28: Verifying Slave DUT
For B_TIMEOUT = 8
  Fails if R_TIMEOUT <= 11
% assume m1s
% prove s1s
S
DUT
R_TIMEOUT = 8
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 29: Verifying Master DUT
For B_TIMEOUT = 8
  Fails if R_TIMEOUT >= 10
% assume s1s
% prove m1s
M
DUT
R_TIMEOUT = 12
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 30: Different Combinations of Safety Time-outs
B_TIMEOUT | R_TIMEOUT | Master Testbench | Slave Testbench
8 | <= 9 | Pass | Fail
8 | 10 or 11 | Fail | Fail
8 | >= 12 | Fail | Pass
For each combination of B_TIMEOUT and R_TIMEOUT, either master or slave testbench fails
Deadlock bug is exposed
Safety is safer for the naïve user!
McMillan’s approach also works, but tedious – see paper
Simplified AXI example (both safety and liveness versions) available at:
http://www.oskitechnology.com/wp-content/uploads/2015/09/fmcad15.tar.gz
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.

## Slide 31: Who Will Check for Soundness?
Can tool developers create a safer methodology?
  End-users focus on writing quality properties and the tools handle the rest?
  Warn users about vacuous proofs
  Warn users about non-standard semantics caused by tool settings
Meanwhile, end-users use safer coding practices
  Coding guidelines related to coding constraints to avoid dead-ends
  Examine formal testbench for unexpected dead-end traces
  Use an appropriate rule for compositional reasoning with liveness properties
    Encourage less sophisticated users to use safety properties instead
© 2015 OSKI TECHNOLOGY, INC. ALL RIGHTS RESERVED.
Notes: Concluding slide

## Slide 32: Thank you!

## Slide 33: Verifying Slave DUT
Checker: master_safety_bready
Constraint: slave_safety_rlast
With B_TIMEOUT = 8 and R_TIMEOUT = 8, no failure
For B_TIMEOUT = 8 and R_TIMEOUT = 12, failed with following waveform
Chart: Master failure (B_TIMEOUT=8, R_TIMEOUT=12)
| 0 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7 | 7 | 8 | 8 | 9 | 9 | 10 | 10 | 11 | 11 | 12 | 12 | 13 | 13 | 14 | 14 | 15 | 15 | 16 | 16 | 17 | 17 | 18 | 18 | 19 | 19 | 20
clk | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12
bvalid | 9 | 9 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10
bready | 7 | 7 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7
rvalid | 5 | 5 | 6 | 6 | 6 | 6 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 6 | 6 | 6 | 6
rlast | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 4 | 4 | 4 | 4
rready | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Master
Slave Constraints
Master
Checkers
S

## Slide 34: Decomposition: Slave Verification
Checker: slave_safety_rlast
Constraint: master_safety_bready
Failed with following waveform
Chart: Slave failure (B_TIMEOUT=8, R_TIMEOUT=8)
| 0 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7 | 7 | 8 | 8 | 9 | 9 | 10 | 10 | 11 | 11 | 12 | 12 | 13 | 13 | 14 | 14 | 15 | 15 | 16 | 16 | 17 | 17 | 18 | 18 | 19 | 19 | 20
clk | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12
bvalid | 9 | 9 | 9 | 9 | 9 | 9 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10
bready | 7 | 7 | 7 | 7 | 7 | 7 | 8 | 8 | 8 | 8 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7
rvalid | 5 | 5 | 6 | 6 | 6 | 6 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5
rlast | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
rready | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Root case: master is not accepting second BVALID
Increase the R_TIMEOUT value relative to B_TIMEOUT
  For B_TIMEOUT = 8 and R_TIMEOUT = 12, failure is gone
Slave
Master
Constraints
Slave
Checkers
S

## Slide 35: Running on Composed System
With B_TIMEOUT = 8 and R_TIMEOUT = 8, system with Master as well as Slave gave show deadlock
Chart: Deadlock failure in the composed design (B_TIMEOUT=8, R_TIMEOUT=8)
| 0 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7 | 7 | 8 | 8 | 9 | 9 | 10 | 10 | 11 | 11 | 12 | 12 | 13 | 13 | 14 | 14 | 15 | 15 | 16 | 16 | 17 | 17 | 18 | 18 | 19 | 19 | 20
clk | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12 | 11 | 11 | 12 | 12
bvalid | 9 | 9 | 9 | 9 | 9 | 9 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10
bready | 7 | 7 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7 | 7
rvalid | 5 | 5 | 6 | 6 | 6 | 6 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5
rlast | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
rready | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2

## Slide 36: Links and References
Download the toy AXI example with both safety and liveness versions of the checks from
http://www.oskitechnology.com/wp-content/uploads/2015/09/fmcad15.tar.gz
[McMillan99]
  K. L. McMillan, “Circular compositional reasoning about liveness”, CHARME 99
[Trefler2000]
  K. S. Namjoshi & R. J. Trefler, “On the completeness of compositional reasoning”, CAV 2000